## Slide 1: زبان توصیف سخت‌افزار
Hardware Description Language

## Slide 2: زبان‌ها
  VHDL
    یادگیری حداقل یک زبان به طور کامل
      یادگیری ناقص و سعی و خطا  سخت شدن توصیف و اشکال‌زدایی
    اصول یکسان – ساختارهای نحوی متفاوت
    VHSIC HDL (اوایل دهة 1980)
    مبتنی بر زبان ADA

## Slide 3: VHDL
کاربردها:
  مستندسازی:
    به جای توصیف زبان طبیعی:
      نادقیق (برداشت‌های مختلف)
      غیر قابل پردازش

## Slide 4: VHDL
کاربردها:
  مدل‌سازی:
    مراحل اولیة طراحی:
      عملکرد و رفتار کلی مشخص است
      توصیف الگوریتم با دستورهای رفتاری
      کمک به فهم صورت مسأله
      جلوگیری از سرایت اشکالات به سطوح پایین طراحی

## Slide 5: VHDL
کاربردها:
  مدل‌سازی:
    مثال: کنترل‌کنندة آسانسور
...
while (true)
begin
...
if (REQUEST = true)then
if (REQUEST_FLOOR > CURRENT_FLOOR) then
MOVE_UP (CURRENT_FLOOR, ...);
else
MOVE_DOWN (CURRENT_FLOOR, ...);
end if;
end if;
...
end;
...

## Slide 6: VHDL
کاربردها:
  سنتز
    تولید خودکار مدار از توصیف
    زیرمجموعة قابل سنتز
      لزوم آشنایی با این زیرمجموعه
      تفاوت ابزارها  portable code
        کد غیر قابل سنتز برای دیگری
        مدار متفاوت
      کلیات یکسان
    این درس:
      موارد کلی مشترک
      تحوة کدنویسی مناسب

## Slide 7: VHDL
کاربردها:
  درستی‌سنجی
    محیط درستی‌سنجی: testbench
    عناصر اصلی:
      طرح مورد آزمون
      تولید و اِعمال بردارهای ورودی
      مشاهده و تحلیل خروجی‌ها

## Slide 8: VHDL
کاربردها:
  درستی‌سنجی
    تولید بردارهای ورودی:
      تصادفی
      انتخاب هوشمندانه
      الگوریتم‌های تولید خودکار بردارهای آزمون (ATPG)
    نیاز به توصیف با کد VHDL
      برنامه‌نویسی روالی
      خواندن از فایل

## Slide 9: VHDL
  مثال:
    سخت‌افزار محاسبة (x2 + y2)1/2
    مقایسه با نتیجة رفتاری
...
1 L1 : L_MODULE(X,Y,L);
⋮
11 LL : process (⋯)
12 begin
13 for X in 0 to 63 loop
14 for Y in 0 to 63 loop
15 begin
16 L_BEHAVE := (X**2 + Y**2)**0.5;
17 if(L != L_BEHAVE)
18 ERROR_SIG <= ’1’;
19 end if;
20 end for;
21 end for;
22 end process LL;
...

## Slide 10: سطوح تجرید (Levels of Abstraction)
رفتاری:
    توصیف عملکرد مطلوب (الگوریتمی)
    بدون پرداختن به مدار
    همة امکانات VHDL
    قابل نمایش با روندنما (flow chart)

## Slide 11: سطوح تجرید

## Slide 12: سطوح تجرید
انتقال ثبات (Register-Transfer Level) RTL:
  مسیر داده
    ثبات‌ها
    مدارهای ترکیبی
    منابع ارتباط دهنده‌ بین آنها
      گذرگاه
      مالتی‌پلکسر
      سیم
      ...
  کنترل‌کننده (مسیر کنترل)
    ماشین حالت متناهی FSM

## Slide 13: سطوح تجرید
انتقال ثبات:
⋮
process(CLK)
begin
if (rising_edge(CLK)) then
DOUT <= not(DOUT);
end if;
if (falling_edge(CLK)) then
if (DIN == ’0’) then
DOUT <= not(DOUT);
end if;
end if;
end process;
⋮

## Slide 14: سطوح تجرید
ساختاری (structural):
begin
FA1:FULL_ADDER port map (C0, A0, B0, S0, C1);
FA2:FULL_ADDER port map (C1, A1, B1, S1, C2);
FA3:FULL_ADDER port map (C2, A2, B2, S2, C3);
FA4:FULL_ADDER port map (C3, A3, B3, S3, C4);
end;
    FULL_ADDER خود ممکن است از گیت‌ها تشکیل شده باشد.

## Slide 15: توصیف سخت‌افزار با VHDL
جزئیات:
  Language Reference Manual
    به عنوان مرجع اصلی
    1076 LRM Ieee Standard Vhdl Language Reference Manual.pdf
  زيرمجموعة قابل سنتز: استاندارد 1076.6
  VHDL-AMS 1076.1
    فقط شبیه‌سازی
    نحوة شبیه‌سازی: معادلات دیفرانسیل

## Slide 16: VHDL Structural Elements
Entity: Interface
Architecture: Implementation, behavior
Configuration: Structure, hierarchy
Process: Sequential Execution
Package: Components (Modular design), Utilities (data types, constants, subprograms)
Library: Group of compiled units, object code

## Slide 17: Entity
entity HALFADDER is port( A, B: in bit; SUM, CARRY: out bit); end entity HALFADDER;
Interface description
No behavior/implementation definition
entity ADDER is port( A, B: in integer range 15 to 0; SUM: out integer range 15 to 0; CARRY: out bit ); end ADDER;
Linking via port signals
  data types
  signal width
  signal direction
in bit_vector (3 downto 0); out bit_vector (3 downto 0);

## Slide 18: Architecture
entity HALFADDER is port( A, B: in bit; SUM, CARRY: out bit); end HALFADDER; architecture RTL of HALFADDER is begin SUM <= A xor B; CARRY <= A and B; end architecture RTL;
Implementation of the design
Always connected with a specific entity
  one entity can have several architectures
  entity ports are available as signals within the architecture
Contains concurrent statements

## Slide 19: Architecture Structure
architecture RTL of STRUCTURE is subtype DIGIT is integer range 0 to 9; constant BASE: integer := 10; signal DIGIT_A, DIGIT_B: DIGIT; signal CARRY: DIGIT;
begin DIGIT_A <= 3; SUM <= DIGIT_A + DIGIT_B; DIGIT_B <= 7; CARRY <= 0 when SUM < BASE else 1; end EXAMPLE ;
Declarative part:
  data types
  constants
  intermediate signals
  component declarations
  ...
Statement part (after 'begin'):
  signal assignments
  processes
  component instantiations
  concurrent statements: order not important
   Simulator recalculates sum any time an operand changes
Port is a kind of signal.

## Slide 20: Entity Port Modes
in:
  signal values are read-only
out:
  signal values are write-only
  multiple drivers
buffer:
  similar to out
  signal values may be read, as well
  only 1 driver
inout:
  bidirectional port
Output port modes have to match.

## Slide 21: Use of VHDL Objects

## Slide 22: Structural Model
  توصيف ساختاري functionality را صريحاٌ توصيف نمي كند بلكه فقط ليستي از اجزا و نحوة اتصال آنهاست.

## Slide 23: Component Declaration
entity FULLADDER is port (A,B, CARRY_IN: in bit; SUM, CARRY: out bit); end FULLADDER; architecture STRUCT of FULLADDER is component HALFADDER port (A, B : in bit; SUM, CARRY : out bit); end component;
component ORGATE port (A, B : in bit; RES : out bit); end component; begin signal W_SUM, W_CARRY1, W_CARRY2 : bit;
. . .
In declarative part of architecture
Can use any name for the components
  but better to use the same as entity name
entity HALFADDER is port( A, B: in bit; SUM, CARRY: out bit); end entity HALFADDER;
entity ORGATE is port( A, B: in bit; RES: out bit); end entity ORGATE;

## Slide 24: Component Instantiation
architecture STRUCT of FULLADDER is component HALFADDER port (A, B : in bit; SUM, CARRY : out bit); end component; component ORGATE port (A, B : in bit; RES : out bit); end component; signal W_SUM, W_CARRY1, W_CARRY2: bit; begin MODULE1: HALFADDER port map( A, B, W_SUM, W_CARRY1 ); MODULE2: HALFADDER port map ( W_SUM, CARRY_IN, SUM, W_CARRY2 ); MODULE3: ORGATE port map ( W_CARRY2, W_CARRY1, CARRY );
end STRUCT;
May need many of each
Instantiation in statement part of architecture (after 'begin')
Wires signals together:
  default: positional association

## Slide 25: Named Signal Association
entity FULLADDER is port (A,B, CARRY_IN: in bit; SUM, CARRY: out bit); end FULLADDER; architecture STRUCT of FULLADDER is component HALFADDER port (A, B : in bit; SUM, CARRY : out bit); end component; . . . signal W_SUM, W_CARRY1, W_CARRY2 : bit; begin MODULE1: HALFADDER port map ( A => A, SUM => W_SUM, B => B, CARRY => W_CARRY1 ); . . . end STRUCT;
Named association:
  left side: "formals" (port names from component declaration)
  right side: "actuals" (architecture signals)
Independent of order in component declaration

## Slide 26: Configuration
architecture … begin
component HALFADDER port(A, B: in bit; SUM, CARRY: out bit); end HALFADDER; signal W_SUM, W_CARRY1, W_CARRY2: bit; · · · MODULE1 : HALFADDER port map(A, B, W_SUM, W_CARRY1);
MODULE2: HALFADDER port map ( W_SUM, CARRY_IN, SUM, W_CARRY2 );
Entities may be instantiated directly without preceding component declaration
(Not recommended)
entity HALFADDER is port( A, B: in bit; SUM, CARRY: out bit); end entity HALFADDER;
entity ORGATE is port( A, B: in bit; RES: out bit); end entity ORGATE;
architecture RTL of HALFADDER is begin
…
end architecture RTL;
architecture RTL of ORGATE is begin
…
end architecture RTL;
Library (work)
for MODULE1: HALFADDER use entity work.HALFADDER (RTL);
for MODULE2: HALFADDER use entity work.HALFADDER (RTL);

## Slide 27: Configuration
Selects entity/architecture pairs for instantiated components
Generates the hierarchy
Default binding rules:
  selects entity with the same name as component
  last compiled architecture is used

## Slide 28: Simple Configuration Specification
entity FULLADDER is port(A, B, CARRY_IN: in bit; SUM, CARRY: out bit); end FULLADDER; architecture STRUCT of FULLADDER is component HA port(A, B: in bit; SUM, CARRY: out bit); end component;
for MODULE1:HA
use entity work.HALFADDER (RTL);
for MODULE2:HA
use entity work.HALFADDER (GATE);
signal W_SUM, W_CARRY1, W_CARRY2: bit; begin MODULE1:HA port map (…, …); MODULE2:HA port map(…, …);
end STRUCT;
entity HALFADDER is
port(A,B: in bit; S, CY: out bit); end A;
architecture RTL of HALFADDER is · · ·
end RTL;
architecture GATE of HALFADDER is · · ·
end GATE;
Library (work)

## Slide 29: Configuration Example
configuration CFG_FULLADDER of FULLADDER is for STRUCT for MODULE2:HA use entity work.HALFADDER(GATE); end for; for others:HA use entity work.HALFADDER(RTL); end for; end for; end CFG_FULLADDER;
Entity/architecture pairs may be selected by use of
  instance names
  'all': all instances of the specified component
  'others': all instances not explicitly mentioned
Possible to reference an existing configuration of a submodule
configuration CONFNAME of ENTITYNAME is
for ARCHNAME
for INSTANCENAME use entity LIBNAME.ENTNAME(ARNAME);
for all:FA use configuration work.CFG_FULLADDER;

## Slide 31
CONFIGURATION average_gate_delay OF d_register IS
FOR latch_based
FOR dr
FOR di : dl
USE ENTITY WORK.d_latch(sr_based);
FOR sr_based
FOR c1 : sr
USE ENTITY WORK.sr_latch(gate_level);
FOR gate_level
FOR g2, g4 : n2
USE ENTITY WORK.nand2_t(average_delay)
END FOR;
FOR g1, g3 : n2
USE ENTITY WORK.nand2_t(less_delay)
END FOR;
END FOR;
END FOR;
FOR c2 : n1
USE ENTITY WORK.inv_t(average_delay)
END FOR;
END FOR;
END FOR;
END FOR;
END FOR;
END average_gate_delay;

## Slide 32: Configuration
سنتز:
  ابزارهای امروزی پشتیبانی می‌کنند
  بعضي از ابزارهاي سنتز جملات configuration را در نظر نمي گيرند و ممکن است قوانين پيش فرض را اعمال کنند.
    در این ابزارها در declarationها:
      نام componentها عين نام entity باشد
      نام، مود و نوع portها عين پورت entity باشد