## Slide 1: Hardware Description Languages
Basic Concepts

## Slide 2: Application of HDLs
VHDL به عنوان زبان مستندسازي (توصيف فرمال و بدون ابهام).
سنتز: تبديل (اتوماتيك يا دستي) يك توصيف به توصيفي با جزئيات بيشتر

## Slide 3
A digital system design process

## Slide 4
Simulation

## Slide 5: VHDL - Overview
Very High Speed Integrated Circuit Hardware Description Language
  Modeling of digital systems
  Concurrent and sequential statements
  Design lifetime > Designer lifetime
  Man- and machine-readable documentation
International Standards
  IEEE Std 1076-1987
  IEEE Std 1076-1993, 2000, 2002, …

## Slide 6: VHDL - History
  2003: VHDL-200X by VASG (VHDL Analysis and Standardization Group)
    Responsible for maintaining and extending the VHDL standard (IEEE 1076).
  2005: Accellera VHDL TSC took over.
  2006: Accellera VHDL-2006-D3.0 approved
    DATE 2007: date_vhdl_tutorial.pdf
  Pure definition of language in the LRM (Language Reference Manual)
  No standards for application or methodology

## Slide 7: VHDL Standards
علاوه بر استانداردهاي خالص, تلاشهايي براي استاندارد كردن عوامل مربوط به VHDL انجام گرفته است:
  پكيج هاي
    Std_logic_1164
    Numeric_bit
    Numeric_std
  زيرمجموعة قابل سنتز: استاندارد 1076.6
  VHDL-AMS 1076.1

## Slide 8: VHDL - Overview
در حال حاضر براي VHDL-AMS فقط شبيه سازي امكان پذير است چون سنتز آنالوگ بسيار پيچيده است.
شبيه سازي Mixed Signal هم مسايل همگام سازي شبيه سازهاي ديجيتال و آنالوگ و الگوريتمهاي حل معادلات ديفرانسيل غيرخطي را دارد.

## Slide 9: VHDL-Application Field
Hardware design
  ASIC: technology mapping
  توصيف به gate-level netlist تبديل مي شود و اجزا از كتابخانة ASIC انتخاب مي شوند.
  FPGA, CPLD: LUT/PAL mapping
  SPLD: smaller structures, hardly any use of VHDL

## Slide 10: Concepts of VHDL
Execution of Statements:
  Sequential
  Concurrent
Methodologies:
  Abstraction
  Modularity
  Hierarchy

## Slide 11: Concepts of VHDL
  Abstraction: طرح را مي توان در سطوح مختلفي از جزئيات توصيف كرد:
      براي مدلسازي، سطوح بالا كافي است.
      براي سنتز، ممكن است جزئيات بيشتري لازم باشد.

## Slide 12: Concepts of VHDL
  Modularity: مي توان بلوك بزرگ پيچيده را به بلوكهاي كوچكتر تقسيم كرد و براي هر بخش يك مدل نوشت.
  Hierarchy: تشكيل يك درخت سلسله مراتبي
      هر كدام از نودها ممكن است در سطح متفاوتي از abstraction توصيف شده باشد.

## Slide 13: Abstraction Levels in IC Design
  VHDL براي سطح layoutمناسب نيست.

## Slide 14: Behavioral Description in VHDL
در VHDL رفتار عملياتي با process مدل مي شود.

## Slide 15: Behavioral Description
collect : PROCESS
BEGIN
WAIT UNTIL serial = '0';
WAIT FOR half_bit;
FOR count IN 0 TO 7 LOOP
WAIT FOR full_bit;
buff (count) := serial;
END LOOP;
WAIT FOR full_bit;
IF serial = '0' THEN
frame_error <= '1';
WAIT UNTIL serial = '1';
ELSE
frame_error <= '0';
dataready <= '1';
parallel_out <= buff;
WAIT UNTIL received = '1';
WAIT UNTIL received = '0';
dataready <= '0';
END IF;
END PROCESS collect;
constant half_bit : time := 50 ns;
constant full_bit : time := 100 ns;

## Slide 16: Dataflow (RTL) Description

## Slide 17: Dataflow (RTL) Description
OUTPUT_REG: process(CLK) begin if CLK'event and CLK='1' then Y <= S1 + S2; Z <= Z_I ; end if ; end process OUTPUT_REG ; end RTL ;
architecture RTL of MOORE_TEST is signal STATE,NEXTSTATE : STATE_TYPE ; begin REG: process (CLK, RESET) begin if RESET='1' then STATE <= START ; elsif CLK'event and CLK='1' then STATE <= NEXTSTATE ; end if ;
end process REG ;

## Slide 18: Abstraction Levels and VHDL

## Slide 19: Structural Description
اجزا ممكن است گيت پيچيده باشند.

## Slide 20: ASIC Development
بعد از شبيه سازي post-synthesis مي توان ماكزيمم فركانس كلاك را تخمين زد (بر اساس مسير بحراني موجود)
بعد از شبيه سازي post-layout مي توان ماكزيمم فركانس كلاك را به دست آورد
Post-layout
simulation
CMOS 45 nm

## Slide 21: Information Content in Abstraction Levels

## Slide 22: Modularity and Hierarchy
  گاهي اوقات simulation model هايي از اجزا يا تراشه هاي استاندارد وجود دارند كه مي توان به طرح خود متصل كرد و نتايج شبيه سازي را در محيط واقعي مشاهده كرد.
Partitioning in several partial designs
  Restrict complexity
  Enable teamwork
  Study of alternative implementations

## Slide 23: Design Tools
Simulation

## Slide 24: Tool Set
Synthesis
Place & Route
Simulation Tools
Timing Analysis
Power Analysis
Verification

## Slide 25: Simulation Tools
Simulation Tools
  Oblivious simulation
  Event-driven logic simulation
  Mixed-language simulation
  Cycle-based simulation
  Post-layout simulation

## Slide 26: Simulation Tools
Types of Logic Simulators:
  Oblivious:
    Simple but inefficient
  Event driven:
    See the world as a series of discrete events
  Cycle-based
    Rough simulation for synchronous sequential designs

## Slide 27: Simulation Concept

## Slide 28: Oblivious Simualtor
Starts by a table and initial values
Evaluates periodically (even when no change in inputs)
  Repeats until nothing is changed in a pass.

## Slide 29: Event-Driven Simulator
Simulates when an event (change) at input(s) of a component
Only part of the design is evaluated

## Slide 30: Event-Driven Simulator
When a gate input changes, it places a transaction (value, delay) on the driver of the delayed signal (e.g. gate output)
  It will expire after delay
   Changes its value
Repeats for other gates with changed inputs
Concurrency is handled.
Mostly used in industry

## Slide 31
RTL:
  At the beginning of each cycle, propagate values from primary inputs and from register outputs into combinational blocks (CBs).
  Compute the stable outputs of CBs, and store them in register inputs (they’ll move to outputs in the next cycle).
CB
CB
CB
RTL model
Cycle-based Simulation

## Slide 32
  Functionality and timing can be verified separately
  Assumption:
    Within each cycle, all signal changes occur in zero-delay
Only evaluate on the clock edge
  First: evaluate all combinational logic
  Next: latch values into state registers
  Repeat on next clock edge
1
0
Cycle 1
Cycle 2
Cycle 3
t
Steady state
Steady state
Steady state
Assume ‘zero-delay’ (don’t care about the transient delays)
Zero-delay cycle-based simulation

## Slide 33
Within each Combinational Block, gates can be levelized (sorted in topological order) for evaluation.
Going by level number, every gate will be evaluated after its inputs have been computed.
So: we order the gates by the flow of data, and we don’t care about the real delays  assume “0 delay”.
Combinational Feedbacks?
A levelized CB
Levelizing the gates

## Slide 34: Event vs. Cycle-Based Simulation

## Slide 35: Cycle-Based vs. Event-Driven
Cycle-based:
  Only boundary nodes
  No delay information
Event-driven:
  Each internal node
  Need scheduling and functions may be evaluated multiple times
Cycle-based does not detect glitches and setup/hold time violations, while event-driven does

## Slide 36
Simulation: Performance vs. Abstraction
.001x
SPICE
Event-driven
Simulator
Cycle-based
Simulator
1x
10x
Performance and Capacity
Abstraction

## Slide 37: Why is it faster?
Node a has 5 transitions and b has 3 transitions.
Event-driven simulator reevaluates when inputs change
 Gate A simulates 5 times,
  Gate B: 9 times,
  Gate C: 6 times
  Total 20 times.
  But for only these 3 gates
Cycle-based simulator simulates the entire circuit only once (at the end of current cycle)
 All Gates in the circuit are simulated regardless whether their inputs have been changed.
Conclusion:
  Event-driven is faster if few transitions (typically less than 5% active nodes).
In practice, experiments confirm that a cycle-based simulator is almost always 5-10 times faster (and uses less memory)
FF
Z
FF
FF
a
b
c
d
A
B
C